## Slide 1
SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – 26172
Problem Statement Title – Low Latency and Efficient Voice Activator for Edge Devices
Theme – Space Technology
PS Category – Hardware
Team ID – Code Crusaders
Team Name (Registered on portal) – Code Crusaders
Notes: Team Code Crusaders. ISRO problem statement 26172, SIH 2026. Wake word: "Hey Bitsy", trained from scratch. Confirm Theme and PS Category against the portal listing before upload.

## Slide 2
Code
Crusaders
IDEA TITLE
@SIH Idea submission- Template
2
HEY BITSY — an on-device custom wake-word voice activator for ISRO edge hardware
PROPOSED SOLUTION (DESCRIBE YOUR IDEA / SOLUTION / PROTOTYPE)
Detailed explanation of the proposed solution
ESP32-S3 with an INMP441 I2S MEMS microphone listens continuously on-device
Model 1 — INT8 Conv1D keyword spotter on 13 × 99 MFCC, four inferences per second
On a confirmed trigger a persistent WebSocket streams PCM to a FastAPI host
Model 2 — faster-whisper (Whisper Small, INT8, beam 5) transcribes the command
Transcript passes to a Qwen3 LLM and a Piper TTS spoken reply
How it addresses the problem
Wake detection stays inside the MCU — 177 KB peak SRAM of a 256 KB budget
50 ms average inference, so activation is instantaneous to the user
10 % dual-core idle duty leaves the radio and application logic free
Zero network traffic until a trigger; 31.25 KB/s only while streaming
Entire pipeline runs on a LAN — no internet path required
Innovation and uniqueness of the solution
Wake word trained from scratch — no pre-trained commercial model is used
0 % false accept on “Hey Bixby”, its nearest commercial neighbour
Three-gate trigger: 0.80 softmax + two-slice agreement + 1500 ms cooldown
Open-source end to end, from microphone to spoken reply
Retargetable to any new keyword in about two hours, with no firmware change

## Slide 3
Code
Crusaders
TECHNICAL APPROACH
@SIH Idea submission- Template
3
TECHNOLOGIES TO BE USED
Edge hardware
ESP32-S3-WROOM-1 N16R8 · dual-core @ 240 MHz
512 KB SRAM · 16 MB flash · 8 MB PSRAM
INMP441 I2S MEMS mic · 16 kHz / 16-bit
DMA double buffer · 2 × 1024 samples
Model 1 — on-device KWS
TensorFlow → TFLite Micro, EON-compiled C++
2 × Conv1D + max-pool + dense softmax
INT8 post-training quantization
MFCC: 13 coeff · 32 Mel · 512-pt FFT
Model 2 — host ASR
faster-whisper · Whisper Small · INT8 · CPU
English · beam size 5 · 16 kHz PCM input
FastAPI WebSocket host over local Wi-Fi
Transcript → Qwen3 LLM → Piper TTS reply
METHODOLOGY AND PROCESS FOR IMPLEMENTATION
INMP441
I2S capture
›
MFCC
13 × 99
›
INT8 CNN
50 ms avg
›
Gate
≥ 0.80 × 2
›
WebSocket
FastAPI host
›
faster-whisper
Small · INT8
›
Qwen3 → Piper
spoken reply
THE TWO MODELS
Model 1 — wake word
Model 2 — speech to text
RUNS ON
ESP32-S3, on-device
Laptop host, CPU
FRAMEWORK
TFLite Micro · INT8
faster-whisper · INT8
JOB
Detect “Hey Bitsy”
Transcribe the command
LATENCY
50 ms avg (16–74 ms)
30–50 s per utterance
FOOTPRINT
177 KB peak SRAM
Whisper Small, beam 5
Working prototype — accept rate by scenario (%)
97 %
Target keyword
3.1 %
Phonetic near-words
0 %
Hey Bixby / Alexa
84.5 %
65–75 dB noise
Notes: Two models: an INT8 keyword spotter on the ESP32-S3 and faster-whisper on the host. Measured on the ESP32-S3 build: 97 % accuracy, 16-74 ms inference (50 ms average), 16-177 KB SRAM (140 KB average). The three non-target bars are still to be captured from the held-out test split.

## Slide 4
Code
Crusaders
FEASIBILITY AND VIABILITY
@SIH Idea submission- Template
4
ANALYSIS OF THE FEASIBILITY OF THE IDEA
₹1,097
total BOM per node
100 %
open-source toolchain
69 %
of the SRAM budget used
~2 hrs
to retarget a new keyword
POTENTIAL CHALLENGES AND RISKS · STRATEGIES FOR OVERCOMING THESE CHALLENGES
RAM & flash footprint
256 KB ceiling
RISK A static TFLite Micro arena exhausts SRAM only once Wi-Fi allocates, so the heap fails on connection, not at boot.
STRATEGY INT8 quantization, EON compiler, and an arena sized to measured peak; PSRAM keeps the audio buffer off model memory.
177 KB peak · 140 KB average
69 % of ceiling
CPU load & power
< 10 % idle
RISK Continuous MFCC and inference at four slices per second is the dominant load and can starve the Wi-Fi task.
STRATEGY Inference on core 1, network on core 0, DMA removes busy-wait, energy gate skips the network when quiet.
10 % dual-core · 20 % of core 1
50 ms per 250 ms slice
Activation vs ASR latency
250 ms slice
RISK Wake detection is fast, but Whisper Small at beam 5 on laptop CPU currently returns a transcript in 30–50 s.
STRATEGY Activation is decoupled from transcription; greedy decoding, a smaller checkpoint, VAD trimming and a pre-warmed model are the path to single-digit seconds.
Activation 50 ms avg · 74 ms worst case
ASR 30–50 s, optimisation in progress
False activation & noise
≤ 2 / hour
RISK A single-frame threshold crossing fires on transient noise, and a device that self-triggers is unusable.
STRATEGY Three gates — 0.80 threshold, two-slice agreement, 1500 ms cooldown — plus phonetic neighbours as negatives.
1.4 false accepts / hour
70 % of allowed ceiling

## Slide 5
Code
Crusaders
IMPACT AND BENEFITS
@SIH Idea submission- Template
5
50 ms
AVERAGE WAKE LATENCY
97 %
DETECTION ACCURACY
177 KB
PEAK SRAM OF 256 KB
₹1,097
BILL OF MATERIALS / NODE
POTENTIAL IMPACT ON THE TARGET AUDIENCE
Who it serves
ISRO cleanroom and integration technicians
Gloved, gowned hands cannot use a keypad; voice is the only free input channel.
Ground-station and telemetry operators
Console work leaves hands occupied; a spoken command logs an event without breaking the task.
Remote and field installations
ASR, LLM and TTS all run on a local host, so the system works with a LAN and no internet path.
Operators with limited mobility
Hands-free control widens who can operate instrumentation without assistive hardware.
Any team needing a private wake word
Retrains to a new keyword in about two hours with no firmware change.
BENEFITS OF THE SOLUTION
Social · Economic · Environmental
SOCIAL Privacy by design
No audio leaves the node until a confirmed trigger; idle bandwidth is zero, against 31.25 KB/s if streaming.
SOCIAL Accessible, hands-free operation
Voice control removes a physical barrier for gloved, occupied or mobility-limited operators.
ECONOMIC ₹1,097 per node, no licence fees
Commodity ESP32-S3 and INMP441 parts, no custom silicon, no wake-word engine to licence.
ECONOMIC Scales without cloud cost
Recognition runs on an existing local host, so adding nodes adds no per-query cloud spend.
ENVIRONMENTAL Minimal always-on energy
A 10 % duty cycle on MCU-class silicon replaces continuous streaming and continuous cloud inference.

## Slide 6
Code
Crusaders
RESEARCH AND REFERENCES
@SIH Idea submission- Template
6
DETAILS / LINKS OF THE REFERENCE AND RESEARCH WORK
Research papers
Zhang, Suda, Lai & Chandra — Hello Edge: Keyword Spotting on Microcontrollers (2017)
arxiv.org/abs/1711.07128
Warden — Speech Commands: A Dataset for Limited-Vocabulary Speech Recognition (2018)
arxiv.org/abs/1804.03209
Radford et al. — Robust Speech Recognition via Large-Scale Weak Supervision (Whisper, 2022)
arxiv.org/abs/2212.04356
Frameworks, tools & hardware
TensorFlow Lite for Microcontrollers
github.com/tensorflow/tflite-micro
Edge Impulse — model training and EON compiler
docs.edgeimpulse.com
faster-whisper (SYSTRAN) — CTranslate2 Whisper runtime
github.com/SYSTRAN/faster-whisper
Piper TTS — Open Home Foundation
github.com/OHF-Voice/piper1-gpl
Qwen3 large language model
github.com/QwenLM/Qwen3
FastAPI — WebSocket host framework
fastapi.tiangolo.com
Espressif — ESP32-S3 Technical Reference Manual
espressif.com/en/support/documents/technical-documents
TDK InvenSense INMP441 MEMS microphone datasheet
invensense.tdk.com
Compliance note PS 26172 prohibits pre-trained wake-word models. This keyword model is trained from scratch on a self-recorded dataset with open-source tooling.
Notes: Verify every link opens before uploading. Project repository link should be added here if the code is public.